## Slide 1
Q-Point Stability For Transistors
PRESENTED BY :- ARYAN DILIPBHAI LANGHANOJA
ENROLLMENT -NO :- 92200133030

## Slide 2: Parts Of Transistors
A typical transistor is composed of three layers of semiconductor materials or more specifically terminals which helps to make a connection to an external circuit and carry the current. A voltage or current that is applied to any one pair of the terminals of a transistor controls the current through the other pair of terminals. There are three terminals for a transistor. They are:-
Base: - This is used to activate the transistor.
Collector: - It is the positive lead of the transistor.
Emitter: - It is the negative lead of the transistor.

## Slide 3: Thickness and Doping of Emitter, Base and Collector
 | Thickness | Doping
Emitter | Wide | Heavily Doped
Collector | More Wide than Emitter | Moderately Doped
Base | Very Thin | Lightly Doped

## Slide 4: Types Of Transistors
Transistors
BJT
N-P-N
P-N-P
FET

## Slide 5: N-P-N Transistor
Symbol In Circuit

## Slide 6
P-N-P Transistor
Symbol In Circuit

## Slide 7: Transistors Configuration
There Are Three Types Of Transistors Configuration-
Common Emitter Transistor (CE)
Common Base Transistor (CB)
Common Collector Transistor (CC)

## Slide 9: Region Of Operation
There Are Four Different types of Operating Regions for transistors:-
Active Region.
Cut-Off Region.
Saturation Region.
Reverse Active Region.

## Slide 10
1) Cut-Off Region
2) Reverse-Active Region
3) Saturation region
4) Active Region

## Slide 11: TYPES OF BIASING
There Are Four Types Of Transistor Biasing.
  Fix Biased
  Fix Biased With Emitter Resistor
  Collector to Base Bias
  Voltage Divider Bias
  Emitter Bias

## Slide 12: FIX-BIAS
In This Figure, Shown that Voltage Given at Base-Emitter Junction is VBB and Voltage Given at Emitter-Base Junction is VEE. We are using active Region of operation.
When we applied Voltage at Emitter, Emitter emits lot of free electron, because it is heavily doped. That Electron Enters in Base. Where some holes are present. And electron combines with them.
Now electron has two choices, go to VBB or to go VCC. Because VCC>>VBB. Some electrons are attracted by VBB and rest all electron is attracted by the VCC. And it is shown that the current is IC due to that. And the current IB is the current produces by the electron attracted by the VBB.

## Slide 13
Now, applying KCL,
IE = IB + IC
As already mentioned that very few electron attracted by VBB
IB  0 and IC  IE

Now ,
 IE = IB + α IE
 IB = IE - α IE
IB = IE - α IE
IB = (1- α) IE
Putting IE = IC / α .
IB = (1- α) IC / α .
 IB = (1- α/ α) IC .
 IC = (α/1- α)IB .
 IC = (α/1- α)IB

Where  is called the current gain.
IC = α IE
Ic = IB

## Slide 14
Now, if we took Emitter-Base Loop and apply
KVL in it,
 VBB- IBRB – VBE = 0.

And Now, if we took Collector-Base Loop and apply
KVL in it,
VCC -ICRC – VCE = 0.
IB = VBB – VBE RB
 VCE = VCC -ICRC

## Slide 15: Observation Table
VCC | RC | IC | VCE
12 V | 1 K  | 11.902 mA | 0.098 V
12 V | 1.01 K | 11.784 mA | 0.09816 V
12 V | 1.02 K | 11.669 mA | 0.09762 V
12 V | 1.03 K | 11.556 mA | 0.09732 V
12 V | 1.04 K | 11.446 mA | 0.09616 V

## Slide 16: Fix Bias With Emitter Resistor
In this condition, the Emitter Resistor RE will act as a feedback resistor. In any situation, temperature changes, then  changes. Let suppose the temperature increases, then  increases, and for the fix current IB, Collector Current IC will increases. Then the voltage drop across emitter Resistor will also increase. and base voltage VBE will also increase. And because of VBE increased VB is also increased and IB will decrease. And Q-point will be stable.

## Slide 17
Now, if we took Emitter-Base Loop and apply KVL in it,
 VBB- IBRB – VBE – IERE = 0.
 VBB- IBRB – VBE – IERE = 0.
 VBB- IBRB – VBE – (IB + IC)RE = 0.
 VBB- IBRB – VBE – (IB + IB )RE = 0.
VBB- IBRB – VBE – (1 +  )IBRE = 0.
And Now, if we took Collector-Base Loop and
apply KVL in it,
VCC -ICRC – VCE - IERE = 0.

IB = VBB - VBE RB + ( + 1) RE
VCE = VCC –IC(RC + RE)

## Slide 18
Observation Table
VCC | RC | IC | VCE
12 V | 1 K | 2.287 mA | 9.713 V
12 V | 1.01 K | 2.287 mA | 9.69013 V
12 V | 1.02 K | 2.287 mA | 9.66726 V
12 V | 1.03 K | 2.287 mA | 9.64439 V
12 V | 1.04 K | 2.287 mA | 9.62152 V

## Slide 19
Chart: COMPERATIVE ANALYSIS
| 10.41 | 10.38705 | 10.366119999999999 | 10.34318 | 10.32024
 | 12.8829 | 12.8829 | 12.8829 | 12.8829 | 12.8829
 | 11.902 | 11.784 | 11.669 | 11.556 | 11.446